## Slide 1
Fire Inspection and Code Enforcement
8th Edition
Inspector I
Chapter 4 — Construction Types and Occupancy Classifications

## Slide 2: Learning Objective 1
Identify construction types.

## Slide 3: Know what AHJ building codes are based upon.
National Fire Protection Association® (NFPA®)
Canadian Commission on Building and Fire Codes®
International Code Council® (ICC®)

## Slide 4: Inspectors need to be aware of job duties related to building codes.
Review plans
Conduct inspections

## Slide 5: Know the types of construction determined by architects or design professionals.
Occupancy type
Building size
Automatic sprinkler systems
Materials used
Material fire resistance
Owner cost
Other factors
Local definitions

## Slide 6: Understand United States construction characteristics.
International Building Code® and NFPA® recognize 5 types of construction
Each type has subcategories, depending on the code and construction type

## Slide 7: Inspectors should be able to recognize common basic building elements.
Structural frame
Load-bearing walls (interior and exterior)
Roof construction
Nonload-bearing walls and partitions (interior and exterior)
Floor construction

## Slide 8: Become familiar with construction materials and their performance under fire conditions.
(Cont.)

## Slide 9: Become familiar with construction materials and their performance under fire conditions.

## Slide 10: Know the characteristics of Type I construction.
All structural members are composed of only noncombustible materials
Structural members possess a high fire-resistance rating
Expected to remain structurally stable during a fire according to fire resistance rating
(Cont.)

## Slide 11: Know the characteristics of Type I construction.
Reinforced and precast concrete
Masonry
Protected steel-frame
Courtesy of Ron Moore and McKinney (TX) Fire Department

## Slide 12: Specific combustible materials in small quantities are occasionally allowed for use in Type I structures.
Roof coverings
Wood trim
Finished flooring
Wall coverings
Look for examples of exceptions in model building codes

## Slide 13: Inspectors have specific concerns regarding Type I construction.
Owner/occupant may install greater amounts of these combustible materials
Unregulated use of certain materials may be prohibited
Some materials contribute to an unacceptable increase in risk

## Slide 14: It is incorrect to refer to Type I construction as fireproof.
Amount of combustible materials in the structure may compromise fire resistance
Incorrect characteristic used to justify reduction in sprinklers
May not, by itself, offer greater life safety or loss reduction
Noncombustible does not mean fireproof

## Slide 15: Type II structures are composed of materials that will not contribute to fire development or spread.
Courtesy of Scott Strassburg
Feature metal framing members, metal cladding, or concrete block walls with metal deck roofs supported by unprotected open-web steel joists
Noncombustible materials that do not meet the stricter requirements for Type I
Used when fire risk is low
Used when fire suppression and detection system designed to meet the hazard load

## Slide 16: Inspectors have specific concerns regarding Type II construction.
The term noncombustible does not reflect the true nature of the structure
Noncombustible buildings often incorporate combustible materials
Combustible features can be exterior, like balconies or wall coverings

## Slide 17: Type III construction is common in churches, schools, apartment buildings, and mercantile structures.
Requires exterior walls be constructed of noncombustible materials
Interior elements determined by adopted code

## Slide 18: Know the common materials used in Type III construction.
Exterior walls and interior nonbearing walls
Floors, roofs, interior nonbearing framing, partitions
Older buildings
New buildings
Brick
Concrete
Reinforced concrete
Small-dimension wood or metal stud systems
Nonbearing wall framing members
Unprotected steel and aluminum
Wood or steel trusses
Wood trusses and floor joist systems

## Slide 19: Inspectors have specific concerns regarding Type III construction.
Voids exist inside wooden channels created by roof and truss systems
Allows fire to spread unless proper fire-stopping is applied
Renovated older structures
Creation of large voids above ceilings and below floors
New construction materials
May result in reducing the load-carrying capacity of the supporting structural member
Change of use
Original use may have changed to one that requires a greater load-carrying capacity

## Slide 20: NOTE
Fire-stopping is required for all construction with vertical or horizontal penetrations.

## Slide 21: Type IV construction is often referred to as heavy-timber construction.
Use of large-dimension timber, greater than 4 inches (100 mm) for all structural elements
Dimensions of all structural elements must adhere to minimum dimension sizing: columns, beams, joists, girders, roof sheathing
Courtesy of Dave Coombs

## Slide 22: Be familiar with characteristics of Type IV construction.
Exterior walls constructed of noncombustible materials
Interior elements are solid or laminated wood; no concealed spaces
Floors and roofs are constructed of wood; generally have no voids
All non-wood materials must have fire-resistance rating of at least 1 hour
Fire-retardant-treated wood framing is permitted within interior wall assemblies

## Slide 23: Type IV structures are more resistant to collapse due to effects of fire.
Heavy-timber structural elements form an insulating effect
Derived from the timbers’ own char
Reduces heat penetration to the inside of the beam

## Slide 24: Understand modern Type IV construction materials.
May include glued-laminated beam
Smaller-dimension lumber that is glued together
Strong
Exhibit the same or improved fire performance characteristics as older solid-sawn beams
Most often used in churches, auditoriums, and other large, vaulted facilities

## Slide 25: Type V construction is commonly known as wood frame or frame construction.
(Cont.)
Exterior bearing walls may be composed of wood and other combustible materials
Brick or stone veneer may be constructed over wood framing
Veneer offers the appearance of masonry-type construction; provides little additional fire protection
Single-family home
Courtesy of Walt Schneider

## Slide 26: Type V construction is commonly known as wood frame or frame construction.
Most often consists of framing materials
Wood 2x4-inch (50 mm by 100 mm) studs or wood sill plates
Sheathing is applied directly to the stud face
Wooden boards or plywood
Oriented strand board (OSB)
Rigid insulation boards
Any combination of these
(Cont.)

## Slide 27: Type V construction is commonly known as wood frame or frame construction.
Exteriors are attached in various ways
Supports have evolved
Siding: nails, screws, or glue
Stucco: spread over screen lattice attached to studs
Lightweight engineered lumber systems support both roof and floor loads
Lightweight wood trusses can be assembled in many configurations
Typically use a triangular configuration for stability
Efficient use of lumber
Provide open areas to install other systems

## Slide 28: Know the disadvantages of truss construction.
Structural redundancy is reduced
All truss members are critical to maintain the strength and stability of the truss
Loss of any member can be catastrophic

## Slide 29: Wood I-joists are efficient at spanning large distances with little material.
Assembly of two wood flanges connected by a wooden web
Web was originally plywood; OSB has become more common
Made of either solid-sawn dimension lumber or engineered wood product such as laminated veneer

## Slide 30: Understand the disadvantages of wood I-joists.
Structural member is light
Susceptible to fire damage
In many cases, web will burn prior to the floor sheathing; results in floor system collapse

## Slide 31: Understand the three types of Canadian construction.
Combustible construction
Does not meet the acceptable criteria for noncombustible construction
Noncombustible construction
Heavy-timber construction
Degree of fire safety is attained by the use of noncombustible materials for structural members and other building assemblies
Avoids concealed spaces under floors and roofs
Degree of fire safety attained through limitations on sizes of wood structural members and thickness and composition of wood floors, roofs
Avoids concealed spaces under floors and roofs

## Slide 32: Know where to find information on the Canadian definitions.
National Building Code of Canada (NBC)
Specifies requirements and limitations on materials used for each type
Lists requirements in table formats
Occupancy classifications
Construction types

## Slide 33: REVIEW QUESTION
How many types of construction are recognized by both the International Building Code® and the NFPA®?

## Slide 34: Learning Objective 2
Identify single-use occupancy classifications.

## Slide 35: An occupancy classification can be defined as the use of all or a portion of a building or structure.
Some occupancies have higher fire loads
Some occupancies have a greater number of occupants
Helps inspection personnel get an idea of hazard level
Developed by model code organizations
Separates occupancies into risk categories
Based on the use of the structure
Some model codes are similar, but inspectors need to understand the differences

## Slide 36: Model codes are grouped according to general descriptions.
Assembly
Business
Educational
Factory/Industrial
Institutional
Mercantile
Residential
Storage
Utility/Misc.

## Slide 37: Inspectors should be aware that building conditions rarely remain the same.
For example, a warehouse or storage area converted to loft apartments
Original fire protection systems no longer adequate
Exit requirements may need to be upgraded to meet higher requirements
(Cont.)

## Slide 38: Inspectors should be aware that building conditions rarely remain the same.
Storage occupancy issues are a frequent cause of substantial loss
Occurs when there is more combustible content than originally used in the building
Design of the fire sprinkler system and other protection features may be inadequate for the additional contents

## Slide 39: When reviewing renovation plans, an inspector needs to answer two questions.
Have the construction materials or the building’s purpose changed since the last inspection?
What effect will those changes have on the fire and life safety provisions for the structure?

## Slide 40: An assembly occupancy is any structure or room that is used for the gathering of 50 or more persons.
Wide variety of uses
Divided into subclassifications based on
Houses of worship
Theaters
Restaurants
Arenas
Type of activities
Perceived hazard associated with activities
Exception used by the NFPA®

## Slide 41: Business occupancies provide a working place for large numbers of occupants in an office environment.
General offices
Medical offices
Air traffic control towers
Municipal buildings
College and university instructional buildings
Dry cleaning and laundry facilities
Barber and beauty shops

## Slide 42: The ICC® and the NFPA® differ slightly on outpatient clinics.
ICC®
NFPA®
Includes outpatient clinics where patients are ambulatory and not incapacitated by anesthetic
Classifies outpatient clinics as ambulatory health care occupancies

## Slide 43: Business occupancies are normally divided into group areas and individual working spaces.
Positive effect
Compartmentalized large spaces
Separates it into fire and smoke zones
Open-plan office spaces
Lose the positive effect
Allows fire and smoke to move unimpeded throughout

## Slide 44: Know the characteristics of an educational occupancy.
Six or more persons
Through the 12th grade
Meet for 4 or more hours in a day or more than 12 hours in a week

## Slide 45: Inspecting educational occupancies present significant challenges.
Wide variety of uses
Labs/Shops: 1 person for every 50 square feet (4.5m2)
Gyms/Lecture Halls/Dining: Follow requirements for assemblies
Also applies to day care facilities that care for 6 or more children older than 2½
Age and capabilities can vary widely
Classrooms: 1 person for every 20 square feet (1.85m2)
(Cont.)

## Slide 46: NOTE
Religious educational rooms and auditoriums associated with a church that have occupant loads of less than 100 are classified with assembly occupancies.

## Slide 47: Inspecting educational occupancies present significant challenges.
Maintenance and other personnel may be in the buildings after hours
Risk of fire considered low to moderate
Pose hazards due to their high occupant loads and wide variety of uses
Each code describes facilities differently
Must be familiar with AHJ’s adopted codes; crucial when determining occupancy loads

## Slide 48: Canadian codes do not classify educational facilities separately.
Grouped with Group A Assembly occupancies
Requirements limiting occupant loads are similar to U.S.
Vocational training facilities require almost double the space per person than the ICC® or NFPA®

## Slide 49: Each model code classifies manufacturing and processing facilities differently.
NFPA®
General Purpose
Special Purpose
High Hazard
ICC®
Hazardous materials/processes not included; may be classified as high-hazard
Evaluate these structures based upon requirements that pertain to primary use

## Slide 50: Canadian codes divide factory and manufacturing facilities into three subdivisions.

## Slide 51: Be familiar with the different codes regarding institutional occupancies.
ICC®
NFPA® 1™ and NFPA® 101®
Group I Institutional
Occupancies that provide care or medical treatment to people with physical limitations due to health or age
Includes penal or correctional facilities
Health Care
Ambulatory Health Care
Detention and Correctional
Residential Board and Care
Day Care (portions of the occupancy requirements)

## Slide 52: Be familiar with Canadian codes for institutional occupancies.

## Slide 53: Health care occupancies provide services to people who cannot evacuate without assistance.
Identified only in NFPA®1™ and NFPA®101®
ICC® codes include similar requirements included as part of Group I Institutional I-2, a subclassification
Canadian codes include similar provisions within Group B Care of Detention Occupancies classification
Differences among the various codes

## Slide 54: Inspectors may find that more than one code applies in institutional/health care facilities.
Adopted local code may apply to the design of the building
Multiple code documents are used to ensure all requirements are met
NFPA® 101® may pertain to areas such as long-term care in order to obtain Medicare certification

## Slide 55: Inspectors need to understand ambulatory health care occupancies.
Buildings or portions of buildings that provide medical services to four or more patients on an outpatient basis
Patients may be incapable of self-preservation due to anesthesia or medication
Urgent care facilities are included in this category
ICC® codes classify outpatient care facilities as Group B Business Occupancies
(Cont.)

## Slide 56: Inspectors need to understand ambulatory health care occupancies.
One-and two-family dwellings are being used as residential care
States may regulate only dwellings with four or more residents
Become familiar with state/provincial legislation for authority

## Slide 57: Detention and correctional facilities are locations where the occupants are held under restraint or security.
As defined in NFPA®1™ and NFPA®101®
In emergency situations, the occupants are prevented from taking anything but limited life-preservation actions
Require direct assistance from staff personnel
ICC® codes include these facilities within the classification of Group I Institutional Subdivision I-3

## Slide 58: Inspectors need to understand residential board and care occupancies.
NFPA® 1™ and NFPA® 101®
Locations where lodging, boarding, and personal care are provided
Four or more residents
Unrelated to the owner or operator
Differentiates these occupancies through the delivery of personal care services to the residents
ICC®
Classify similar occupancies within Group I Institutional or Group R Residential
Canadian
Employ either the Group B Care or Detention Occupancies or Group C Residential Occupancies
(Cont.)

## Slide 59: Inspectors need to understand residential board and care occupancies.
Staff responsibilities
Safety and welfare of the residents
Do not provide medical or nursing care
Provide meals
Ensure they have taken medicine
Monitor well-being
Evacuation capacities
Classified as slow, prompt, or impractical
Inspector duties
Be familiar with changes that may occur regarding proper classification of occupants

## Slide 60: Inspectors need to be familiar with the characteristics of day care occupancies.
Provide care, maintenance, and supervision
Persons of any age
Less that 24 hours per day
Someone other than a relative or legal guardian provides client care
Numbers of clients that establish these occupancies differ in each code
Other regulating agencies may have requirements that differ from the locally adopted code

## Slide 61: Each code differs in how it classifies of day care occupancies.
NFPA®101®
Separate classification category
ICC®
Group E Educational
Group I Institutional Subdivision I-4

## Slide 62: Understand inspection considerations for day care occupancies.
Must be tailored to meet the specific needs of residents
Understand capabilities of the occupant groups
Best way to observe and mitigate potential fire and life safety hazards
Look at age and physical condition of population

## Slide 63: Model codes define a mercantile occupancy as any building that is used to display or sell merchandise.
Includes department stores, pharmacies, supermarkets, shopping centers, malls, other retail locations
Contain large quantities of combustible materials
Potential for high life loss
Merchandise, displayed and stored, can result in high fire loads and restrict exit access
Product displays can be moved which can alter the original automatic sprinkler discharge patterns

## Slide 64: All model codes require residential occupancies meet minimum fire and life safety requirements.
Definition
Requirements separate from building code
NFPA® categories
Provide sleeping accommodations under conditions other than those defined for health care or detention facilities
One- and two-family dwelling codes
One- or two-family dwelling
Lodging and rooming house
Hotel
Dormitory
Apartment building

## Slide 65: Understand one- and two-family dwelling occupancies.
NFPA®1™ and NFPA® 101®: Structures that have no more than two dwelling units, including detached units, semidetached units, and duplexes
Occupancy classifications determined by degree of fire separation between units
Not exempted in model codes, however not subject to periodic inspections in most jurisdictions
Homeowners may request municipal inspections

## Slide 66: Lodging (boarding) and rooming houses are facilities that provide sleeping accommodations for rent.
NFPA® 1™ and NFPA® 101® and IFC® (International Fire Code®) definition
Guest houses, foster homes, bed and breakfasts
ICC® and Canadian codes
Similar to those within the broader occupancy classification of Group R Residential
Guest houses
Foster homes
Bed and breakfasts
Motels
Motels that provide 24-hour accommodations for 16 or fewer individuals without cooking facilities

## Slide 67: Understand the characteristics of a boarding or rooming house.
Usually a separate, distinct occupancy
If a building shares space, with intermingled operations, the most restrictive codes apply
Cannot be located above a mercantile unless it is separated by a 1-hour fire-separation barrier

## Slide 68: New rooms are often created in areas that were not designed to serve in that capacity.
Inspector will find that exit halls have been converted to sleeping/living areas
Modifications may block or eliminate exit passageways
Must verify that the maximum number of residents does not exceed sixteen individuals
If temporary occupancies, remember occupants are unfamiliar with surroundings
Additional signage, maps showing exit paths, and additional fire protection features may be needed

## Slide 69: Hotels present a wide range of fire and life safety challenges for the inspector.
Model codes define a hotel as a building or group of buildings that provide sleeping rooms for transient guests

## Slide 70: NOTE
Transients are often defined as persons staying in an occupancy for less than thirty days.

## Slide 71: Hotels often include many other occupancies.
Meeting rooms
Convention areas
Casinos
Ballrooms
Theaters
Restaurants and kitchens
Bars and lounges
Storage areas
Swimming pools
Physical fitness centers
Boutique retail shops
Business offices
Parking garages
Mechanical spaces
(Cont.)

## Slide 72: Hotels often include many other occupancies.
Inspection considerations
Requirements and challenges that each occupancy classification or use poses to the rest of the facility
Only applicable when occupancies are not separated from other elements
ICC® and Canadian codes
Do not have occupancy categories that differentiate hotel uses
Each code describes these occupancies within the broader residential group classification
ICC®: Group R Residential Occupancies
Canadian: Group C Residential Occupancies

## Slide 73: Understand the characteristics of dormitory occupancies.
Building or portion of a building that provides sleeping accommodations
16 or more persons who are not related
Sleeping accommodations may be in one room or series of smaller rooms
Individual cooking facilities not provided
Cafeteria or dining hall may be present
Residential fraternity houses may fall into this category according to the ICC®

## Slide 74: Become familiar with apartment building occupancies.
May be single or multistory structures
Contain three or more independent dwelling units
Equipped with cooking and bathroom facilities
Units may have direct access to exterior or interior corridors that lead to protected or unprotected stairways
More than seven stories may be considered high-rise structure; require higher levels of protection
Courtesy of Ron Jeffers

## Slide 75: Each apartment building presents a unique set of problems to a fire inspector.
Unique issues
Building features
Inspection concerns
Location
Structure age
Age and economic status of the occupants
Fire protection features must be evaluated based upon risk levels in each building
Design features must be maintained
Keep records to use as reference for all inspections
Additions to the building; verify proper fire separations
Changes in use; usually require increased fire and life safety requirements

## Slide 76: Each model code approaches storage occupancies in somewhat different ways.
Generally structures used to store goods, merchandise, vehicles, or animals
NFPA® uses a broad approach that includes warehouses, storage units, freight terminals, aircraft hangars, grain elevators, barns, stables
ICC® codes describe storage within several occupancy classifications; Group S Storage and Group H Hazardous classification
Must be familiar with locally adopted code and amendments to adequately conduct an inspection
(Cont.)

## Slide 77: Each model code approaches storage occupancies in somewhat different ways.
Classifications
Method of storage employed also considered
Inspection
Combustibility or flammability of contents inside a storage facility usually used
Evaluate a change to more combustible contents or storage methods
Make sure the fire sprinkler system and other protection features are adequate for changes

## Slide 78: The utility/miscellaneous classification is used for structures that do not fit any other classification.
Only recognized by ICC®
Generally, incidental structures to primary occupancy
May not pose a hazard
Barns
Livestock shelters
Carports
Towers
Sheds
Fences over 6 feet (1.8 m) in height
Retaining walls

## Slide 79: REVIEW QUESTION
What are the single-use occupancy classifications?

## Slide 80: Summary
An inspector’s ability to determine the construction type and occupancy classification of a structure is a critical part of an inspection.
The architect or construction engineer evaluates the construction materials and determines the construction type.
(Cont.)

## Slide 81: Summary
The appropriate occupancy classification must be assigned during the plans review process and verified when the certificate of occupancy is issued before the owner/occupant takes possession of the structure.
During periodic inspections, the inspector should note any changes in use and contents.
(Cont.)

## Slide 82: Summary
When alterations to the structure are made, an inspector must ensure that the fire and life safety requirements are not compromised.
Model building and fire codes provide the inspector with the guidelines for ensuring that life safety requirements are met.
(Cont.)

## Slide 83: Summary
Because the information in this chapter is general in nature, inspectors must become familiar with their locally adopted codes.