## Slide 1
Essentials of Fire Fighting
6th Edition
Firefighter II
Chapter 15 — Fire Hose

## Slide 2: Learning Objective 1
Describe the safety considerations taken when service testing a fire hose.

## Slide 3: Service testing fire hose guidelines are provided in NFPA® 1962.
Should be performed
Before testing, examine for
If defects found – Tag for repair
If damage not repairable – Remove from service
Annually
After repairs
After vehicle has run over hose
Excessive wear, damage to jacket
Coupling damage
Defective, missing gaskets

## Slide 4: The test site area should meet certain criteria before performing testing.
Paved area with enough room to lay out hose in straight lines, free of kinks, bends, or twists
Protected from vehicular traffic
Well lighted
Smooth and free from rocks and debris
On a slight grade to aid water drainage
Complete with water source sufficient for charging hose

## Slide 5: You should also gather the necessary equipment before beginning the test.
Hose testing machine, portable pump, or fire department pumper equipped with gauges
Hose test gate valve
Means of recording hose numbers and test results
(Cont.)

## Slide 6: You should also gather the necessary equipment before beginning the test.
Tags or other means to identify sections that fail
Nozzles with shutoff valves
Means of marking each length with year of test

## Slide 7: The service test procedure requires that you exercise great care.
(Cont.)

## Slide 8: CAUTION
All personnel operating in the area of the pressurized hose should wear at least a helmet as a safety precaution.

## Slide 9: The service test procedure requires that you exercise great care.
Connect hose to discharges
Close all valves slowly
Test lengths of 300 feet (100 m) or shorter
Lay large-diameter hose flat before charging
Stand away from discharge valve connection
Keep area as dry as possible

## Slide 10: REVIEW QUESTION
What are the safety considerations that should be taken when service testing a fire hose?

## Slide 11: Summary
Beyond the understanding of fire hose necessary of a Firefighter I, advancing to Firefighter II includes knowledge of the procedures for testing hose.

## Slide 12: Learning Objective 2
Service test a fire hose.
This objective is measured in Skill Sheet 15-II-1.