## Slide 1
Fire Inspection and Code Enforcement
8th Edition Inspector I
Chapter 7 — Means of Egress

## Slide 2: Learning Objective 1
Describe means of egress systems.

## Slide 3: Know the importance of means of egress for life and safety.
Ability of occupants to evacuate a structure rapidly and safely during a fire or other emergency is a crucial aspect of building design
(Cont.)

## Slide 4: Know the importance of means of egress for life and safety.
Many lives have been lost during emergencies because exits were locked, blocked, or poorly marked

## Slide 5: Know the common factors still being cited despite improvements in fire protection and code revisions.
Examples of code violations
Locked or blocked exit doors
Improperly designed or marked exits
Inaccessible exits
Inadequate or nonexistent fire protection systems
Combustible interior materials contents
Overcrowded occupancies
Courtesy of Rich Mahaney and Scott Strassburg

## Slide 6: Means of egress is one of the most important factors inspectors must consider.
Elements
The exit access
The exit
The exit discharge
Must work together to allow occupants to safely exit from anywhere in a structure during an emergency

## Slide 7: Means of egress systems rely on a number of subsystems to protect and guide occupants during their escape.
Active fire protection
Passive fire protection
Exit signs
Exit illumination
Door hardware
Handrails

## Slide 8: According to NFPA® 101 ®, Life Safety Code®, the means of egress system may pass through a variety of places.
Intervening room spaces
Doorways
Corridors
Passageways
Balconies
Ramps
Stairs
Courts
Yards
Horizontal exits

## Slide 9: The means of egress must terminate in a public way or an area of refuge.
A public way is a street, alley, or similar parcel of land
A public way must also have a clear width and height of 10 feet (3 m)
Essentially open to the outside that is used by the public
(Cont.)

## Slide 10: The means of egress must terminate in a public way or an area of refuge.
An area of refuge should provide protection to those occupants who cannot evacuate a building
Can be located in an approved elevator lobby or a rated stairwell
(Cont.)

## Slide 11: The means of egress must terminate in a public way or an area of refuge.
Should be separated and resist the passage of smoke
If two-way communication is required, the inspector should verify that communication devices are present and in working order

## Slide 12: Be aware of the ways the ADA requirements may affect areas of refuge.
Americans with Disabilities Act (ADA); 1990
Required areas of refuge in some occupancies as a way to protect people who are mobility impaired
Design must meet requirements of ICC/ANSI 117.1, Standard on Accessible and Usable Buildings and Facilities, from International Code Council®/American National Standards Institute

## Slide 13: All of the elements of a means of egress must be free from obstructions and combustible materials.
Exit access
Aisle within an assembly occupancy designed to accommodate and guide people to an exit
Common path of travel leading from inside to an exit
Unenclosed ramp or stairs
Occupied room or space
Leads from occupied portion of a building or structure to the exit
Corridor leading to the exit opening
(Cont.)

## Slide 14: All of the elements of a means of egress must be free from obstructions and combustible materials.
Exit
Protected path consisting of components constructed of approved fire-resistance-rated assemblies
Doors at ground level that lead directly to the outside of the building
Exit passageway to the outside
Horizontal exit
Smokeproof enclosure
Separated from the area of the building from which escape is to be made

## Slide 15: Inspectors need to know the characteristics of exit passageways.
(Cont.)
Exit passageways
Designed to connect interior exit stair or hallway without stairs on the same level to an exit door on the structure's exterior
Must be constructed of the same fire-resistant-rated material as the exit stairs
Constructed in a horizontal plane
Similar to exit stair enclosure

## Slide 16: Inspectors need to know the characteristics of exit passageways.
Exit passageways
Must be wide enough to accommodate the total capacity of all exits that discharge through it
Must be calculated using the expected occupant load for that portion of the structure and not just the immediate occupant load
In large-area buildings, can be used to shorten the travel distance to an exit

## Slide 17: Understand how and why horizontal exits are used.
Commonly used in high-rise buildings and hospitals as a means of passing through a fire-barrier wall that separates two fire compartments in a structure
May be substituted for other exits if they do not compose more than 50 percent of the total exit capacity of the building

## Slide 18: Becomes familiar with the basic types of horizontal exits.
Means of egress from one building to area of refuge in another building on approximately the same level
Means of egress through a fire barrier or fire wall to area of refuge in the building on approximately the same level that provides protection from smoke and fire

## Slide 19: Horizontal exits require fire walls or fire-barrier walls with at least a 2-hour fire-resistance rating.
1½-hour fire-rated door assembly would be installed in the fire barrier to permit movement between the two compartments
Doors must swing in the direction of exit travel, so double doors are required if the area on both sides of the wall is used as part of the means of egress

## Slide 20: Inspectors need to know the characteristics of smokeproof enclosures.
Stairways or stair enclosures designed to limit penetration of smoke, heat, and toxic gases into the stairway
Provide highest degree of fire protection for stair enclosures that the model codes require
Sometimes referred to as smoke towers
Pressurization or use of ventilation can make a stair enclosure smokeproof
Occupants enter through a vestibule or outside balcony

## Slide 21: Exit discharges are the portion of a means of egress that is between the exit and a public way.
Exterior walkway along the side of a structure from the exit to a public way
Privately owned drive or alley that connects the exit to a public way
Inspectors frequently discover that exit discharges are blocked or cluttered

## Slide 22: Inspectors have many responsibilities when it comes to components of means of egress.
Verify that doors, stairs, and walls conform to the adopted building and safety codes
Recognize and evaluate building components that serve as components of a means of egress
Be aware of any exemptions in the means of egress requirements that are permitted in structures that are protected by automatic sprinkler systems

## Slide 23: Fire-resistance-rated assemblies and components provide occupants with separation from products of combustion.
Doors
Walls
Ceilings
Floors
Stairs
Ramps
Panic hardware
Handrails
Guardrails

## Slide 24: Know the two most important life safety functions of doors.
Separate occupants from the movement of fire, smoke, and other toxic gases
Serve as components of a means of egress system

## Slide 25: NOTE
Exit doors also provide a means of access for fire and emergency services personnel.

## Slide 26: Means of egress doors must be constructed so that the way of exit travel is obvious.
Exit doors may be required to open in the direction of travel toward the primary exit, depending on occupancy and occupant load
Each door opening must be wide enough to accommodate the number of people expected to travel through the door in an emergency

## Slide 27: Understand model code requirements in new buildings.
Width
Exceptions exist
Floor on each side must be level
Door must not open over a set of stairs
Exit doors must open easily
Refer to NFPA® Life Safety Code® or applicable building code
Must provide minimum of 32 inches (800 mm) of clear unobstructed width

## Slide 28: Know the exit requirements for buildings with a higher level of significance.
50 or more people are in a room or occupancy
Doors that open into corridors or hallways must be placed so the door does not obstruct more than half of the required exit width during any point in its swing

## Slide 29: Building codes allow a variety of security options for entrance and egress doors.
Become familiar with the operation and acceptance of different types of locking hardware
Locking hardware allows exit doors to remain locked from the outside but still permits slightly delayed or unrestricted egress at all times
Other security devices cause exit doors to remain locked until activated by fire detection, waterflow, or other alarm devices

## Slide 30: Be familiar with common locking hardware.
Panic hardware
Bolt locks
Access-controlled egress
Delayed egress
Electromagnetically locked
Special locking

## Slide 31: Panic hardware may be required based upon occupancy classification and occupant load.
Occupants should be able to operate panic hardware
Setting the door in motion by applying a force of no more than 30 pounds (133.45 N)
Alarms
Causing the latch to release by applying a force of no more than 15 pounds (66.72 N)
Opening exit doors sometimes activates an alarm

## Slide 32: Model building codes define the types of door locks that may be installed.
Used in in buildings that do not require panic hardware
Mostly, exit doors can feature deadbolt locks
Thumb-turn bolts that operate independently of the door latch are examples of unacceptable locking devices
Manually operated flush bolts or surface bolts are not permitted
Tubular deadbolt lock like this one is not acceptable

## Slide 33: Access controls allow occupants to egress freely while enabling the door to be secured from the outside.
Must use security card or enter a code to gain entrance
Requirements
Sensor on the egress side
Doors must be arranged to unlock from a manual unlocking device
Activation of the building fire alarm, fire detection or automatic sprinkler system will unlock the doors
Some entrance doors may not be allowed to be secured
Loss of power to the hardware unlocks door

## Slide 34: Know the characteristics and requirements for delayed egress.
Characteristics
Minimum force requirements to operate
Requirements
Doors unlock upon operation of automatic sprinkler system or automatic fire detection system
Doors unlock when power is lost
Opening the door will activate an audible signal
Doors must be labeled
Occupants must not have to pass through more than one door equipped with delayed egress before reaching an exit

## Slide 35: Know the characteristics and requirements for electromagnetic locks.
May be used on doors in the means of egress that are not otherwise required to have panic hardware
Doors must have listed hardware that incorporates a built-in switch
Hardware is a basic system that detects a push and supplies power to the mag-lock
Card readers or punched-in codes are not needed to gain access
(Cont.)

## Slide 36: Know the characteristics and requirements for electromagnetic locks.
System requirements
Listed hardware that is affixed to the door and has an obvious method of operation
Must be capable of being operated with one hand
Operation of the hardware releases to the electromagnetic lock and immediately unlocks the door
Loss of power to the hardware automatically unlocks the door

## Slide 37: Have a basic understanding of special locking situations.
Examples
Health care facilities
Characteristics
Drug and alcohol rehabilitation
Mental health or memory care units
Alarm devices, key pads, or similar staff-activated devices control exit door locks
A loss of power in the facility allows the doors to open

## Slide 38: Be familiar with self-closing doors and latching doors activated by alarms.
Self-closing doors
Walls separating connected buildings
Walls that separate two different occupancy use groups
Usually held open by magnetic devices
Close automatically to provide a smoke or fire barrier in a fire-barrier wall
Examples
Openings into mechanical or electrical spaces

## Slide 39: Be familiar with requirements for security bars or grilles.
Operation of locks on the egress side of the security bars must conform to the requirements for exit doors
Horizontal sliding or vertical security grilles at the main exit must be operable from the inside without the use of a key
Where two or more exits are required, no more than half of the exists can be equipped with security grilles
During periods of occupancy, grilles must remain secured in the full-open position

## Slide 40: Fire-resistant-rated walls are used to separate designated exits from other parts of the building.
Fire-resistance rating
Building height
Type of building construction
Whether the building has an automatic sprinkler system
Age of building
Modifications
Look for concealed penetrations
Type of occupancy
Become familiar with building codes that were in effect when the structure was originally built
May require changes in exit-wall requirements

## Slide 41: The type of occupancy group also dictates the wall finish.
Class A (0–25 flame-spread rating) interior finishes in exits or exit-access corridors
Class B (26–75 flame-spread rating) interior finishes in exits or exit-access corridors

## Slide 42: The type of occupancy group also dictates the wall finish.
Class A (0–25 flame-spread rating) interior finishes in exits or exit-access corridors
Class B (26–75 flame-spread rating) interior finishes in exits or exit-access corridors

## Slide 43: Ceilings complete the enclosure for the exit or exit-access corridor.
Walls may extend to the bottom of the roof deck or floor above, or to the ceiling of the exit
Ceilings may conceal wiring and HVAC ductwork, or act as a return-air plenum
Ceiling that is part of a means of egress must have the same fire-resistance rating as the walls

## Slide 44: Floor coverings are a frequent source of concern due to the flammability of the materials.
Floor coverings must meet flame- and smoke-generation tests for the given means of egress
Unapproved materials are often used during remodeling; pay particular attention to these areas
Must be installed according to the locally adopted code

## Slide 45: Stairs that serve as part of the required means of egress must meet strict requirements.
Requirements
Other requirements also increase safety during both emergency and nonemergency use
Multistoried buildings
Fire-resistance rating of the enclosure
Separation when exterior stairs are utilized
Exit stairs are critical components of the means of egress
(Cont.)

## Slide 46: Stairs that serve as part of the required means of egress must meet strict requirements.
Stair treads must be solid and slip resistant
Landings must be provided so that no flights of stairs are greater than 12 feet (3.5 m) high
Handrails may be required for both sides of the stairs
Exceptionally wide stairs may be required to have intermediate handrails in the middle
Stair treads and risers must be in good condition to prevent tripping

## Slide 47: Fire-resistant construction must separate interior stairs from other parts of the building.
Three stories or fewer
Construction that encloses the exit must have at least a 1-hour minimum fire-resistance rating
Minimum applies whether the stories connected are above or below the story at which the exit discharge begins
Four or more stories
Separating construction must have a fire-resistance rating of at least two hours
There are some exceptions; consult the locally adopted code

## Slide 48: A self-closing and latching fire-resistance-rated exit door must protect any opening in the exit stairs.
Stairway door must be rated properly, depending on the height of the building
The only permissible openings in exit stairs are those that allow people to enter the stairs from inside the building and those that empty to the exit discharge

## Slide 49: Exterior stairs may serve as exit stairs if they meet the adopted code requirements for outside stairs.
Open stairs used as part of the means of egress are only allowed in buildings equipped with an automatic sprinkler system
These areas must remain clear so that egress is not impaired
Inspectors should verify that exit stairways are not used for any purposes other than as a means of egress

## Slide 50: Inspectors need to understand requirements for ramps.
Became common in many occupancies in the U.S. with adoption of the Americans with Disabilities Act (ADA) of 1990
Each model code addresses requirements in a similar manner
Fire-resistance-rated construction must enclose and protect exterior ramps
Exterior ramps must offer same degree of protection as exterior stairs
Consult provisions of locally adopted code and amendments

## Slide 51: Know the characteristics and requirements for fire escape stairs, ladders, and slides.
External fire escape stairs
On existing buildings, they may constitute only half of the required means of egress
Inspection concerns
Poorly maintained and rusted through
Not properly secured to the wall
Snow-covered or icy
Exposed to high winds
Cluttered with garbage and other debris
Inaccessible due to locked or secured access windows and doors
May not be used as part of means of egress in new construction
(Cont.)

## Slide 52: Know the characteristics and requirements for fire escape stairs, ladders, and slides.
Occupant safety
Each of the model codes provides detailed guidelines for the protection of openings that expose fire escape stairs
To avoid trapping occupants, fire escape stairs must be exposed to the smallest number of door or window openings as possible
Windows
When used for this purpose, they must open with a minimum of effort, or, in some cases, open outward in a manner that does not obstruct the exit path
May be used as access to fire escapes in existing buildings if they meet certain criteria
(Cont.)

## Slide 53: Know the characteristics and requirements for fire escape stairs, ladders, and slides.
Access to stairs must be directly from a balcony, landing, or platform
Ladders only allowed for limited purposes if approved by the AHJ
Slides, also called slidescapes, may be used as ameans of egress where authorized
Must be of an approved type and rated at one exit unit per slide with a rated capacity of 60 persons

## Slide 54: Know the requirements for exit illumination.
When codes require exit illumination, the illumination must be continuous during periods of occupancy
If a single lighting unit such as a bulb fails, the other lights must continue to function so the area is not left in darkness
Battery-operated units may not be used for primary exit illumination but instead as backup supplies

## Slide 55: Know the requirements for emergency lighting.
Design and requirements
Required in certain occupancies
Batteries or auxiliary power system
Must provide proper amount of illumination for 90 minutes
Floors must be illuminated at no less than 1 foot-candle (10 lux) at floor level
Reduction of 0.2 foot-candle (2 lux) is permitted in auditoriums, theaters, concert or opera halls, and other places of assembly during performances
Provides illumination when normal power is lost

## Slide 56: Markings are signs that direct occupants to the nearest exit.
Required in most occupancies
Illuminated exit signs must be positioned so no point in the exit access is more than 100 feet (30 m) from the nearest visible sign
Letters on exit signs must be at least 6 inches (150 mm) high and the principal strokes of the letters at least ¾-inch (19 mm) wide
Courtesy of Dennis Marx

## Slide 57: Exit signs may be wired into the building electrical system or be self-illuminating.
Wired exit signs must have an auxiliary power source — usually an internal battery – or a separate electrical circuit powered by an auxiliary power supply such as a generator

## Slide 58: Know the requirements for floor proximity signs.
Popular in some jurisdictions and are required in some occupancy classifications
Placed to allow occupants to identify location of an exit as they crawl along a floor
Floor-level signs used in addition to standard ceiling-level signs; not a substitute
NFPA® Life Safety Code® and other model codes include location specifics
Requirements for illumination and character size are the same as other exit signs

## Slide 59: Be familiar with the test procedures for both the auxiliary power supplies and emergency lighting systems.
Can originate from batteries, generator
Generator
Codes require monthly and annual test of the system
Review documentation to verify that tests have been conducted as specified
Used to power emergency lighting and exit signs
Connected to building’s electrical system by switchover device
Natural gas, LPG, or diesel fuel may be used
Test procedures

## Slide 60: NOTE
IFC Section 604.5 requires the building owner to document the test results and make the records available to the inspector.

## Slide 61: REVIEW QUESTION
What are the three elements of a means of egress?

## Slide 62: Learning Objective 2
Explain the way to calculate occupant loads for a single-use occupancy.

## Slide 63: Model codes help building officials or plans examiners in determining occupancy.
Codes provide an accepted way to determine how many people can safely exit a structure during an emergency
Means of egress cannot function effectively when the total occupant load has been exceeded

## Slide 64: Inspectors need to understand occupant load.
Total number of persons for which the means of egress of a building or portion thereof is designed
Occupant load is established during plans review process
Design professional typically calculates the proposed occupant load
Plans examiner verifies the calculations

## Slide 65: Inspectors must be able to verify the occupant load of existing occupancies during field inspections.
All inspectors should be familiar with the methods for completing these calculations
In particular, they must be able to verify a new occupant load when a structure changes occupancy classification
Verify that the occupant load for a given location is still correct and posted
Any increase in occupant load must be supported by building design; verification that the means of egress is sufficient
Because each occupancy classification is different, any change in occupancy may also change exit requirements

## Slide 66: NOTE
A change in occupancy classification should initiate a plans review and a new certificate of occupancy.

## Slide 67: Know what information is required to determine occupant load.
Minimum width of each means of egress
Capacity of each individual means of egress
Total capacity of all means of egress
Number of exits required
Maximum travel distance to an exit

## Slide 68: One part of calculating occupant load is similar for each of the model codes.
Each code assigns an occupant load factor per person based on the function of the space
Occupant Load = Net Floor Area ÷ Area per Person (Factor)
Maximum floor area allowed per person stated in square feet (m2)

## Slide 69: Know where to find the maximum floor area allowances.
(Cont.)

## Slide 70: Know where to find the maximum floor area allowances.

## Slide 71: Understand the terms used when figuring “square feet per occupant”.
Gross
Net
Entire square footage (m2) of a space measured wall to wall with no deductions for desks, files, movable partitions, or other items
Gross square footage (m2) minus any space taken up by equipment, furniture, corridors, or other space that is not used for the occupancy

## Slide 72: NOTE
There are other factors that affect the occupant load calculations beyond the locally adopted fire code. For example, bathroom facilities affect the number of people who can reasonably occupy a space. The inspector should check with the local building official before posting a new occupancy limit.

## Slide 73: REVIEW QUESTION
What information is needed to determine the occupant load for a single-use occupancy?

## Slide 74: Summary
Analysis of fires dating back over a century has shown that inadequate or blocked exits have been a significant factor in the loss of lives.
These tragic events have resulted in model code requirements for means of egress for all types of occupancy classifications.
(Cont.)

## Slide 75: Summary
The means of egress routes must conform to the requirements of the locally adopted building and fire code.
Equally important, emergency responders must be able to gain access to the structure.
(Cont.)

## Slide 76: Summary
An inspector is responsible for verifying that building occupants have an unimpeded ability to evacuate a structure or move to an area of refuge within the structure.
This ability is especially important for persons who are mobility impaired or who are not otherwise capable of seeking safety on their own.